## Slide 1: Building a Device Profile
2022 Tech Talk Series
Presentation and resources available @
https://wiki.edgexfoundry.org/display/FA/EdgeX+Tech+Talks

## Slide 2: JAMES BUTCHER james@iotechsys.com
IOTech Systems, Product Manager
  Global B2B edge software products company
  Manage IOTech’s Edge Xpert product
  Previously IOTech Solutions Architect
  Dedicated to product usability
EdgeX Foundry, TSC Chair (2022+)
  Core Working Group Chair (2021-2022)
  Test/QA Working Group Chair (2020-2021)

## Slide 3: EdgeX Tech Talk Series 2022
May 24 - Getting Started with EdgeX
  How to start your journey using EdgeX Foundry for your IoT/edge solutions
June 7 - Build an Application Service
  Learn how to build a custom EdgeX application service using the EdgeX application functions SDK
June 14 - Build a Device Service
  Learn how to build a custom EdgeX device service using the EdgeX device service SDKs
June 21 - Build a Device Profile
  Device Profiles define sensors and devices for EdgeX.
  Learning to write a device profile allows you to connect new sensors or devices to EdgeX without code
June 28 - Getting Started with Snaps
  Presented by Canonical
  Learn how to deploy and orchestrate EdgeX with snaps

## Slide 4: Agenda
What is an EdgeX Device Service (Reminder)
EdgeX Device Profile Overview
  Device Information
  Device Resources
  Device Commands
How to Create a Device Profile
  Modbus power meter example
  Creating a Modbus Device Profile
  Onboarding the Modbus Device to EdgeX
Tooling to Simplify the Work: Device Configuration Tool (DCT)
  Modbus example with DCT
EdgeX Ready program and Device Profile Verification
Further Assistance and Commercial Device Support from the EdgeX ecosystem
  Where to learn more and get help
Q&A

## Slide 5: EdgeX Device Service Reminder

## Slide 6
Core Services
Application Services
Device Services
Core Data
System Management
Reverse Proxy
Secret Store
Additional Security Services
Command
Meta Data
Registry & Config
eKuiper
(Rules Engine)
Scheduler
Alerts & Notifications
CLI
SM Agent
“Northbound” Cloud and IT infrastructure
Additional Services
Supporting Services
Security Services
EdgeX UI (demo only)
“Southbound” OT Devices, Sensors, Cameras and Control Systems
Bi-Directional | Configurable Pipelines | Store & Forward | Filtering | Batching
EdgeX Device Services
Additional Security Services
Additional Security Services
Additional Services
Additional Services
REST
Virtual
CoAP
MQTT
Modbus
SNMP
Add’l
DS
GPIO
Add’l
DS
Add’l
DS

## Slide 7: What is an EdgeX Device Service?
Connects the rest of EdgeX with a device or sensor
  Typically, a physical sensor or device (a “thing” in IoT)
    Examples: a vibration sensor, thermostat, camera, moisture sensor, …
  Can be a virtual sensor or other system made to look like a sensor
    Example: getting the weather from the Internet or data passed from another edge gateway
A device service speaks a particular protocol
  Uses that protocol to communicate with the sensor/device
  Example protocols: Modbus, BACnet, GPIO, MQTT, REST, BLE, …

## Slide 8: Role of a Device Service
A device service has two (2) primary jobs
  Get/collect sensor data from a sensor/device into EdgeX
    Example: get the temperature and humidity readings from a thermostat
  Set/actuate a device on behalf of EdgeX (or EdgeX’s user)
    Example: set the thermostat’s cooling or heating point
A device service has other jobs too
  Transform the sensor data into EdgeX formatted messages (normalizing)
  Monitor the device/sensor (is the device still connected and functioning?)
  Discover new sensors/devices and make them available to EdgeX
    Automatic discovery is protocol dependent and referred to as “provisioning”

## Slide 9: Existing Device Services
EdgeX comes with a number of device services that speak the popular IoT protocols
  Modbus, BACnet, SNMP, MQTT, REST, GPIO, RFID/LLRP, ONVIF camera, USB camera, CoAP, Grove
  Some written in Go and some in C
    Language doesn’t matter because you typically don’t touch the code of the existing services
  “Configure” these to get them to work with your sensor/device
    Low or No code approach – saves integration effort
EdgeX even comes with a “virtual device” to simulate other sensors/devices
3rd party providers offer additional device services (typically commercially)
  For proprietary protocols (ex: Profinet) and for more complete protocol implementation

## Slide 10: EdgeX Device Profiles

## Slide 11: Device Profile Overview
A Device Profile can be thought of as a template, type or classification of a Device
Provides general characteristics for the types of data a device sends and what types of commands or actions can be sent to the device
Includes 3 parts:
  Device Information: identify the device - description, manufacturer, model, labels, etc
  Device Resources: define the device characteristics or data points that the device has – for example a thermostat might record temperature, humidity, etc, and have a writable set point
  Device Commands: how to command the device to get and set values
A device profile is described in YAML or JSON
Device Profiles and Devices are analogous to Class and Objects in software engineering terminology

## Slide 12: Big Picture Steps: Onboarding a Device
Add a device profile to Core Metadata so EdgeX knows the device content info
Add a device entity to Core Metadata so EdgeX knows the physical device info (IP address, Port, Baud Rate, etc)
The Core Metadata services notifies the Device Service a device has been created
The user can then execute read or write commands to access the real device
Device Service events are published to the internal EdgeX Message Bus so consumption by interested subscribers (App Service, Core Data, Supporting Services etc)
Core Services
Core Data
Command
Meta Data
REST
MQTT
Modbus
Device Services
Device Profile
Device

## Slide 13: Device Information / Device Types
Identification Information. Not actually inspected by the device service
  Device name
  Device description
  Device manufacturer
  Device model
  Device labels list that can be used when searching device profiles
name: ElsnerWeatherStation
description: Detecting light and temperature levels
manufacturer: Elsner
model: PO3-Modbus
labels:
- Weather
- LightLevel
- Temperature

## Slide 14: Device Resources
A Device Resource specifies an individual value within a device that can be read or written to
The name and properties sections ensure that the modelling is protocol independent
  Only the attributes section is Modbus (or BACnet, MQTT, OPC UA, etc) specific
The “isHidden” flag relates to the automatic creation of Core Commands for this resource (more later)
deviceResources:
-
name: Temperature
description: Current temperature detected by the sensor
isHidden: false
properties:
valueType: Uint16
readWrite: R
units: Degrees Celsius
attributes:
primaryTable: INPUT_REGISTERS
startingAddress: 1
Common Information
Protocol-Specific Information

## Slide 15: Device Resources – Property Value Fields
Property Value Fields |  |  | 
Field | Mandatory (M) or Optional (O) | Description | Valid Values
valueType | M | The data type of the value | Bool, Int8 - Int64, Uint8 - Uint64, Float32, Float64, String, Binary, Object, Arrays
readWrite | M | Indicates whether the value is readable or writable | R, W, RW
units | O | Indicates the unit of the values: degrees, mm, percentages, etc | String
scale | O | Factor by which to multiply a reading before it is returned | Numeric
offset | O | Value to be added to a reading before it is returned | Numeric
base | O | Value to be raised to the power of the raw reading before it is returned | Numeric
mask | O | Binary mask applied to an integer reading | Numeric
shift | O | Number of bits to shift the integer reading to the right | Numeric
defaultValue | O | Value used for SET command which do not specify one | Numeric
minimum | O | Minimum value when setting | Numeric
maximum | O | Maximum value when setting | Numeric

## Slide 16: Device Resources – Attribute Value Fields (for Modbus)
Attribute Value Fields |  | 
Field | Description | Valid Values
primaryTable | The data type of the value | HOLDING_REGISTERS INPUT_REGISTERS COILS DISCRETE_INPUT
startingAddress | The address in the Modbus device | Numeric
isByteSwap | The Modbus Device Service uses big-endian format. Defines whether to swap the byte on reading little-endian data to transform to big-endian format | Boolean
isWordSwap | Defines whether to use 16-bit segments, also known as words, to re-order the byte sequence with big-endian or little-endian formats | Boolean
rawtype | Optional. Defines the binary data read from the Modbus device and uses a value descriptor data type to identify the data type that the user wants to receive | String
stringRegisterSize | Optional. Used for defining the capacity of the device resource for String data | 1-123 inclusive

## Slide 17: Device Commands (Optional)
Give control over the potential accessing of multiple Device Resources at the same time, either for logical or optimization reasons
(From previous slides) a Device Resource with “isHidden” false will automatically have a singular command generated for it that the Core Command Service is able to invoke (EdgeX V2 optimization to improve / simplify the profiles)
EdgeX Auto Events can invoke Device Commands on a repeating / periodic basis
Again, the “isHidden” flag relates to the automatic creation of commands available in Core Command Service
deviceCommands:
-
name: GetSensorValues
isHidden: false
readWrite: R
resourceOperations:
- deviceResource: Temperature
- deviceResource: LightLevel

## Slide 18: Worked Example

## Slide 19: Modbus Power Meter
Datasheet: https://www.dentinstruments.com/wp-content/uploads/2021/04/PS3037-dent-datasheet-single-page.pdf
User Manual: https://www.dentinstruments.com/wp-content/uploads/2021/04/PS3037_Manual.pdf

## Slide 20: Starting Out: Use a Base File and add Identify Information
name: Network-Power-Meter
manufacturer: Dent Instruments
description: Power Scout Meter
model: PS3037
labels: [modbus, powerscout]
If creating a new device profile, good to start with an existing file as a basis
wget https://docs.edgexfoundry.org/2.2/walk-through/EdgeX_CameraMonitorProfile.yml
First, define how we want to identity this device profile – name, description, etc
Reminder: meta data here not interpreted by EdgeX

## Slide 21: What Sensor Values and Data Points Do We Want to Acquire?
The device’s user manual will tell you what values the device provides
Keep it simple and model only the relevant attributes
  Noting that EdgeX 2.2 (Kamakura) just added support to add/edit/delete Device Resources to a Device Profile on-the-fly
For this power meter example, let’s focus on:
  Current (amps)
  Power (kWh)
  Voltage (volts)
  Energy (kW)
  Demand Window Size (minutes) 15 by default
  Line Frequency (hz) 50 or 60
These will all be Device Resources in our Device Profile

## Slide 22: Accessing the Current Value
name: Current
description: Average current of all phases
isHidden: false
properties:
valueType: Uint16
readWrite: R
units: amps
attributes:
primaryTable: HOLDING_REGISTERS
startingAddress: 8
Holding Registers start at 40000 and Modbus addressing is zero based, so 40009 equates to a Modbus startingAddress value of 8 in our Device Resource
We know it’s a single word with standard unsigned 16 bit integer addressing

## Slide 23: Accessing the Energy Value
name: Energy
description: System Total True Energy
isHidden: false
properties:
valueType: Float32
readWrite: R
units: kWh
attributes:
primaryTable: HOLDING_REGISTERS
startingAddress: 4000
Holding Registers start at 40000 and Modbus addressing is zero based, so 44001 equates to a Modbus startingAddress value of 4000 in our profile
Energy here spans two registers – Least Significant Word (LSW) and Most Significant Word (MSW). This can be read as a single Float32 value

## Slide 24: Do we want to access multiple values at a time?
The data is largely in two categories with perhaps different requirements in terms of data collection:
  Current (amps)
  Power (kWh)
  Voltage (volts)
  Energy (kW)
  Demand Window Size (minutes)
  Line Frequency (hz)
These will be Device Commands in our Device Profile
Configuration, only occasionally changing,
read and writable
Values, regular periodic measurement data, read-only

## Slide 25: Accessing the Values and Configuration
deviceCommands:
- name: Values
isHidden: false
readWrite: R
resourceOperations:
- deviceResource: Current
- deviceResource: Energy
- deviceResource: Power
- deviceResource: Voltage
- name: Configuration
isHidden: false
readWrite: RW
resourceOperations:
- deviceResource: DemandWindowSize
- deviceResource: LineFrequency
The Device Service may choose to optimize accessing these device resources (implementation and protocol dependent)

## Slide 26: Running the Example
Use the real device or a Modbus simulator programmed with the correct registers

## Slide 27: Running the Example
curl http://localhost:59881/api/v2/deviceprofile/uploadfile -F file=@/home/james/EdgeX/PowerMeter.yaml
curl http://localhost:59881/api/v2/device -H "Content-Type:application/json" -X POST \
-d '[
{
"apiVersion": "v2",
"device": {
"name": "Power-Submeter-Device",
"description":"Power Submeter device",
"labels":[
"power submeter",
"modbus TCP"
],
"adminState": "UNLOCKED",
"operatingState": "UP",
"protocols": {
"modbus-tcp": {
"Address": "172.17.0.1",
"Port": "1502",
"UnitID": "1",
"Timeout" : "5",
"IdleTimeout" : "5"
}
},
"serviceName": "device-modbus",
"protocolName":"modbus-tcp",
"profileName": "Network-Power-Meter",
"autoEvents": [
{
"interval": “60s",
"onChange": false,
"sourceName": "Configuration"
},
{
"interval": "5s",
"onChange": false,
"sourceName": "Values"
}
]
}
}
]'
Tip: verify the yaml file is valid
http://www.yamllint.com/
I used edgex-compose with Modbus to generate a docker-compose.yml

## Slide 28: Ease-of-Use with Tooling
IOTech Device Configuration Tool (DCT)

## Slide 29: Why do we need Tooling for this?
Potential issues with the manual approach:
  Requires a specific knowledge of the syntax
  Typos and copy / paste errors
  Syntactic errors
  Updating all references
Benefits of tooling
  Can greatly simplify the effort involved, saving time and money
  Helps eliminate typos and syntactic errors
  Abstract the technicalities of YAML and JSON into intuitive GUI format
  No longer just for software engineers

## Slide 30: Device Configuration Tool (DCT)
Signup at https://dct.iotechsys.com
Commercial IOTech tool but free for EdgeX users!

## Slide 31: DCT Step 1: Create a Device Type
Create a new Device Type. Choose the protocol:

## Slide 32: DCT Step 1: Create a Device Type

## Slide 33: DCT Step 2: Create a Device Resource
Pick an existing Device Type, and click add new Device Resource
The attributes are protocol specific and based on the Device Type (Modbus in this case):

## Slide 34: DCT Step 3: Create the Device Profile
Pick an existing Device Type, and give the new Device Profile a name
Note that a single Device Type can have multiple Device Profiles (i.e. different combinations of Device Resources that you want to expose)

## Slide 35: DCT Step 3: Create the Device Profile
Select which Device Resources are needed in this specific Device Profile

## Slide 36: DCT Step 3: Create the Device Profile
Select the make up of any Device Commands – which Device Resources do we want to get/set together

## Slide 37: DCT : Other Time-Saving Features
Import existing Device Profiles into the DCT
Export as V1 or V2, in YAML or JSON formats (Great for migrating between EdgeX versions)
Export in other formats – e.g., Digital Twin Definition Language
Import Device Resources in CSV file format – many device manufacturers can provide this information which can help reduce time and effort even further

## Slide 38: The EdgeX Ready Program
Highlights the ability of EdgeX users and adopters to work with EdgeX
You earn your EdgeX Ready designation by going through a self-assessment process
Today, the self-assessment process requires an EdgeX adopter to:
  Get and run an instance of EdgeX and associated services
  Create and validate a device profile that represents their device
  Use the profile with an EdgeX device service to provision a device and send sensor data into EdgeX
DCT performs the role of validating Device Profile syntax
Submit your materials (participation form, device profiles, sample sensor data) to the Certification Group
https://wiki.edgexfoundry.org/display/FA/EdgeX+Ready

## Slide 39: Going Further
More Assistance and Commercial Device Connectivity

## Slide 40: IOTech / Edge Xpert Provides Commercial Device Connectivity for EdgeX
Based on EdgeX Device Services but enhanced, productized and ruggedized for industrial use
  Additional features e.g., automatic discovery where possible
  Performance upgrades
  Robust and deployment-ready
Most not available in open source
Can be used with EdgeX or Edge Xpert

## Slide 41: Edge Xpert Value-Add: Modbus
IOTech Value-Add
Device Service is re-implemented in C (compared to Go-Lang EdgeX version):
  Faster Read/Write Access
  Better scalability
  Reduced Footprint
Batch (multi) read and write operations for faster data rates
Supports more devices, e.g., requiring byte & word swapping on all Modbus types
Tested and deployed on wide variety of real Modbus devices
IOTech technical support and expertise
Prevalent in Industrial Automation and Buildings Management
Available in EdgeX Foundry as open source Device Service

## Slide 42: Edge Xpert Value-Add: BACnet
IOTech Value-Add
Automatic discovery (don’t need to create device profiles) and onboarding of devices
Batch/multi read and write operations for faster data rates
Supports more devices via additional types and objects
Supports BACnet Change of Value (COV) for subscription-based updates
Tested and deployed on wide variety of real BACnet devices
IOTech technical support and expertise
Prevalent in COTS devices in HVAC, access control and safety
Available in EdgeX Foundry as open source Device Service

## Slide 43: Resources
Docs
  docs.edgexfoundry.org
    https://docs.edgexfoundry.org/2.2/microservices/device/profile/Ch-DeviceProfile/
    https://docs.edgexfoundry.org/2.2/examples/Ch-ExamplesAddingModbusDevice/
Device Configuration Tool (Free for EdgeX Users)
  https://dct.iotechsys.com
Slack
  edgexfoundry.slack.com (#device-services channel)
EdgeX YouTube Channel
  www.youtube.com/channel/UC30DbbsoqbkGJYJ5omJJsng
Social Media
  Email Forum  https://lists.edgexfoundry.org/mailman/listinfo
  Twitter  https://twitter.com/EdgeXFoundry
  LinkedIn  https://www.linkedin.com/company/edgexfoundry/

## Slide 44: EdgeX Tech Talk Series 2022 Reminder – Come back and see us
May 31 - Getting Started with EdgeX
  How to start your journey using EdgeX Foundry for your IoT/edge solutions
June 7 - Build an Application Service
  Learn how to build a custom EdgeX application service using the EdgeX application functions SDK
June 14 - Build a Device Service
  Learn how to build a custom EdgeX device service using the EdgeX device service SDKs
June 21 - Build a Device Profile
  Device Profiles define sensors and devices for EdgeX.
  Learning to write a device profile allows you to connect new sensors or devices to EdgeX without code
June 28 - Getting Started with Snaps
  Presented by Canonical
  Learn how to deploy and orchestrate EdgeX with snaps

## Slide 45: Tech Talk Feedback
Q&A
Tech Talk Feedback
  Let us know how we did
  Let us know what other topics you’d like to see
  Email:
    info@edgexfoundry.org
    james@iotechsys.com